## Tutorial 2 - P2P WiFi Groups w/ Automatic IP Address

Following tutorial was done with Raspbian 10 Buster and hostapd 2.7

Steps A2.1.x and A2.2.x are EXACT THE SAME AS THE TUTORIAL 1!

Step B2.3.x add the new instructions (Install DNSMASQ).

----------------------------------------------------------------------
Recommendation:
----------------------------------------------------------------------
DO NOT use your main system disk (sdCard), instead, use a fresh system
or some "learn/lab/test" system to makes theses tutorials/experiments.
After completing all set of 3 tutorials you should be able to have
a good basic understanding of the whole matter, and should be able
to know the best way to use the knowledge...

Text Editor:
Use the text editor of your preference, like
Geany (GUI based) or Nano (terminal based), etc.
----------------------------------------------------------------------

----------------------------------------------------------------------
##### A2.1.0 WiFi between 2 peers (or more) w/ automatic IP Address.
----------------------------------------------------------------------

-----
##### A2.1.1 Install hostapd software
-----
sudo apt install hostapd

Temporarilly shutdown hostapd service

sudo service hostapd stop

Unmask (unlock) hostapd service

sudo systemctl unmask hostapd.service
sudo systemctl enable hostapd.service

-----
##### A2.1.2 Create/Modify hostapd configuration file (/etc/hostapd/hostapd.conf)
-----
sudo nano /etc/hostapd/hostapd.conf

Copy and Paste the following text

interface=wlan0
driver=nl80211
hw_mode=g
channel=6
wmm_enabled=0
macaddr_acl=0
auth_algs=1
ignore_broadcast_ssid=0
wpa=2
wpa_key_mgmt=WPA-PSK
wpa_pairwise=TKIP
rsn_pairwise=CCMP
ssid=YOUR-SSID
wpa_passphrase=YOUR-PASSPHRASE-PASSWORD

-----
##### A2.1.3 Edit the file /etc/hostapd, modify the variable "DAEMON_CONF".
-----
Find the line with "#DAEMON_CONF=",
Remove any "#" sign at the beginning of the line, if it exist.
add the following value:

DAEMON_CONF="/etc/hostapd/hostapd.conf"

-----
##### A2.1.4 Edit the file /etc/dhcpcd.conf, give the WIFI an static IP Address
-----

sudo nano /etc/dhcpcd.conf

Add the following lines at the end of the file.

interface wlan0
static ip_address=192.168.50.1/24
nohook wpa_supplicant

-----
##### A2.1.5 Start/Restart hostapd service
-----

sudo service hostapd start

-----
##### A2.1.6 Reboot the system
-----

Reboot the system, so that you can use the installed software.

----------------------------------------------------------------------
##### A2.2.0 Add Internet Routing to the peers.
----------------------------------------------------------------------

-----
##### A2.2.1 Edit /etc/sysctl.conf, allow IPv4 FORWARD
-----

Find the line "#net.ipv4.ip_forward=1", then, remove the sharp (#) signal,
at the start of the line. The sharp (#) signal means that this instruction
is not active, the computer does not read lines starting with sharp (#)...

The line then becomes:

net.ipv4.ip_forward=1

This step will require a reboot.
This step will require a reboot.
The next time the system start it will be able to route traffic (forward)
between peers and the Internet.

-----
##### A2.2.2 Run the following iptables command line instructions
-----

sudo iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
sudo iptables -A FORWARD -m conntrack --ctstate RELATED,ESTABLISHED -j ACCEPT
sudo iptables -A FORWARD -i wlan0 -o eth0 -j ACCEPT

Change the "eth0" and "wlan0" and use the names of your actual interfaces.
Use the command "ip a" to display the actual names of your interfaces.

Every time the computer REBOOT, you will need to run these lines!

----------------------------------------------------------------------
##### B2.3.0 Install DNSMASQ (DNS Forwarder and DHCP Server)
----------------------------------------------------------------------

-----
##### B2.3.1 Install dnsmasq software
-----

sudo apt install dnsmasq

Temporary stop dnsmasq service

sudo service dnsmasq stop

-----
##### B2.3.2 Edit /etc/dnsmasq.conf
-----

sudo nano /etc/dnsmasq.conf

Add following lines at top or end

interface=wlan0
dhcp-range=192.168.50.50,192.168.50.100,255.255.255.0,24h

-----
B2.3.3 Restart/start dnsmasq service
-----

sudo service dnsmasq start

Congratulations,
now you can connect peer-guests without the
need of manual procedure to assign IP ADDRESS.

Just choose SSID and enter password/passphrase.

About DNSMASQ
The software dnsmasq provides 2 basic services: DHCP Server and DNS Forwarder.
The DHCP is the portion that gives a new IP ADDRESS for every
new peer-guest that connects to the network.
The DNS Forwarder provider a forward function to the your internet provider
dns server function (just a kind of linkage).